## Slide 1: Mitigating the Memory Bottleneck with Machine Learning-Driven and Data-Aware Microarchitectural Techniques
Rahul Bera
Doctoral Examination
01.10.2025
Advisor:
Onur Mutlu (ETH Zurich)
Co-Examiners:
Aamer Jaleel (Nvidia Research)
Boris Grot (University of Edinburgh)
Chris Wilkerson (Intel)
Daniel Jiménez (Texas A&M University)
Pradip Bose (IBM T. J. Watson Research Center)
Notes: Hi everyone, I am Rahul. Today I am going to give you a comprehensive overview of my doctoral thesis, titled “...”
So, let’s get started ...

## Slide 2: Modern Workloads Exhibit Massive Data Footprints
High-performance computing
Graph analytics
Large-scale artificial intelligence
Genome analysis
Notes: As we know, many modern workloads from key application domains
such as high-performance computing to genome sequencing exhibit massive data footprints [CLICK]

## Slide 3: Modern Workloads Exhibit Massive Data Footprints
High-performance computing
Graph analytics
Large-scale artificial intelligence
Genome read mapping
Memory is (and likely will be)
the key performance & energy bottleneck
Massive data footprints
overwhelm state-of-the-art memory systems
Notes: Which easily overwhelms the storage and retrieval capabilities of state-of-the-art memory systems
[CLICK] as a result, memory is, and likely will be, the key performance and energy bottleneck of computing systems.

## Slide 4: Numerous Microarchitectural Techniques to Address the Memory Bottleneck
Cache management policies
Dead block prediction
Cache bypassing
Hit/miss prediction
Software prefetching
Spatial prefetching
Temporal prefetching
Thread-based precomputation
Runahead execution
Out-of-order execution
Coarse-grained multithreading
Simultaneous multithreading
Load value prediction
Memory renaming
Memory dependence prediction
Load address speculation
Load address precomputation
Memoization
Dead instruction elimination
Notes: Researchers have proposed numerous microarchitectural techniques to address..
that have constantly pushed the performance and energy efficiency of modern high-performance processors

## Slide 5: Key Observation
Decisions they make online are often
agnostic to the data they observe
Even though microarchitectural techniques
observe a large amount of
Application data
(e.g., program counter value, memory addresses, memory values)
System data
(e.g., bandwidth usage,
cache utilization and pollution)
Notes: However, we observe that:
[CLICK] even though modern microarchitectures observe
a large amount of application data as well as system-generated data during their course of operation
[CLICK] the decisions they make online are often agnostic to the data they observe

## Slide 6: Key Observation
Limited adaptation to observed data
Make decisions based on rigid, and often myopic, human-crafted heuristics, disregarding the large volume of data present at runtime
Insufficient exploitation of data characteristics
Do not fully exploit or often disregard diverse properties of
application data (e.g., criticality, value locality, compressibility)
Decisions they make online are often
agnostic to the data they observe
Data-agnostic decision making
limits effectiveness
Notes: In this thesis, we demonstrate two concrete cases of data-agnostic behavior:
[CLICK] First, we show that many microarchitectural techniques have limited adaptation capability to the observed data
Essentially, they make decision based on ...
[CLICK] Second, we show that many microarchitectural techniques
do not fully exploit or often outright disregard
diverse ... such as ...
We observe that this data-agnostic behavior significantly limit the effectiveness of many state-of-the-art techniques

## Slide 7: Thesis Statement
Adapt its policies by continuously learning
from application data and system-generated data
Tailor its decisions by exploiting characteristics
of application data
By enabling microarchitecture to
We can significantly improve performance and
energy efficiency of state-of-the-art processors
Notes: In this thesis, we posit that, if we enable microarchitecture to
[CLICK] adapt its policies ...
and
[CLICK] tailor its decisions by
[CLICK] we can significantly ...

## Slide 8: Our Approach
Adapt its policies by continuously learning
from application data and system-generated data
Tailor its decisions by exploiting characteristics
of the application data
Exploit lightweight and practical
machine learning methods
Study and exploit
underexplored data characteristics
Notes: To substantiate this hypothesis, we approach in two ways.
[CLICK] First, we exploit lightweight and practical ... to enable microarchitecture to adapt to its policies
[CLICK] Second, we study and exploit previously-underexplored application data characteristics
to enable state-of-the-art microarchitecture to tailor its decisions

## Slide 9
Fetch & Decode
Execute
Access Memory
Commit
Notes: To this end, this thesis makes four key contributions throughout the processor execution pipeline

## Slide 10: Key Contributions
Fetch & Decode
Execute
Access Memory
Commit
Hermes [MICRO’22]
Off-chip prediction (OCP)
using perceptron learning
Athena [under review]
Prefetcher-OCP coordination
using reinforcement learning
Constable [ISCA’24]
Safely eliminating load instruction execution
by exploiting load address-value stability
Pythia [MICRO’21]
Hardware data prefetching
using reinforcement learning
Notes: [CLICK] First, we propose Pythia, a RL based hardware data prefetcher
[CLICK] Second, we propose Hermes, a perceptron-learning-based off-chip load prediction mechanism
[CLICK] Third, we propose Athena, a RL-based approach to coordinate prefetching and off-chip prediction
[CLICK] Fourth, we propose Constable, a safe load execution elimination technique by exploiting load instruction characteristics

## Slide 11: Key Contributions
Fetch & Decode
Execute
Access Memory
Commit
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Hermes [MICRO’22]
Off-chip prediction (OCP)
using perceptron learning
Athena [under review]
Prefetcher-OCP coordination
using reinforcement learning
Constable [ISCA’24]
Safely eliminating load instruction execution
by exploiting load address-value stability
Pythia [MICRO’21]
Hardware data prefetching
using reinforcement learning
Notes: So, now let’s start with Pythia, which is a RL-based hardware data prefetcher.

## Slide 12: What is a Hardware Data Prefetcher?
Predicts address of future memory requests and fetches their data before the program needs them
Typically correlates access patterns in past memory requests with program feature
Program feature  access pattern
When the program feature repeats, the prefetcher anticipates
the repetition of the same access pattern and predicts future addresses
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
(e.g., load PC)
Notes: What is data prefetching? It’s a well-explored technique that predicts
A prefetcher typically correlates access patterns ...
The key idea is: when the program feature repeats, the prefetcher ...

## Slide 13: Three Limitations in Prior Prefetchers
Reliance on a single, fixed program feature
for prefetch prediction
Rigidity limits dynamic adaptation in workloads where
the selected feature provides poor correlation with access pattern
Lack of inherent system awareness
Neglecting a prefetcher’s undesirable effects on the system (e.g., bandwidth usage, cache pollution) often harms performance
Lack of in-silicon customizability
Rigid hardware structure provides no customizability to select
new program features and/or prefetching objective at runtime
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Even though literature is rich with numerous prefetching techniques,
we observe three key limitations that significantly affects their effectiveness
[CLICK] First, most prior prefetchers rely on single ...
This rigidity limits dynamic adaptation across wide range of workloads
[CLICK] Second, many prior prefetchers lack inherent awareness to system-level feedback
which often harms performance in resource-constrained systems.
[CLICK] Third, they lack in-silicon customizability. Their rigid hardware design provides less opportunity
to customize ...

## Slide 14: Our Goal
Design a holistic prefetching framework that can
Learn to prefetch using multiple program features
and inherent system-level feedback information
Be easily customized in silicon to change
program feature and/or prefetching objective on-the-fly
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: To alleviate these challenges, we aim to design a holistic prefetching framework that can
...

## Slide 15
Key Idea: Formulate prefetching as reinforcement learning
Pythia
Processor and Memory System
RL agent
Environment
Autonomously learn
what to prefetch
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Towards this, we propose Pythia, whose [CLICK] key idea is to formulate prefetching as a RL problem.
[CLICK] Pythia itself acts as the RL agent, whose goal is to ... by interacting with its environment which is
[CLICK] the processor ...

## Slide 16
Key Idea: Formulate prefetching as reinforcement learning
Pythia
Processor and Memory System
State
Action
Reward
Program features
(e.g., PC, page offset, cacheline delta)
Prefetch offset
(i.e., delta between the prefetch and demand cacheline)
Prefetch quality
considering system-level feedback
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Pythia extracts a set of program features from the current and past demand requests
and use it as a state information
[CLICK] to take a prefetch action. An action is a prefetch offset that it adds
to the current demand cacheline address to generate prefetch request.
[CLICK] For every generated prefetch request, Pythia gets a numerical reward from the environment
which evaluates the prefetch request under various system-level feedback.
Pythia uses this reward to learn correlation between the state and the action
to autonomously and adaptively generate prefetch requests

## Slide 17
Two-part evaluation
Hardware prototyping
using Chisel
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Trace-driven simulation
using ChampSim
Notes: We evaluate Pythia using both trace-driven simulation and hardware prototyping [NEXT]

## Slide 18
Trace-driven simulation
using ChampSim
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
SPP [Kim+, MICRO’16]
Bingo [Bakshalipour+, HPCA’19]
MLOP [Shakerinava+, DPC3’19]
SPP+DSPatch [Bera+, MICRO’19]
SPP+ PPF [Bhatia+, ISCA’20]
Wide range of prefetchers
Wide range of system-configurations
150 single-core workloads from SPEC CPU 2006, 2017, PARSEC, and Ligra
270 multi-core workload mixes
Wide range of workloads
#cores: 1 – 12 cores
Main memory bandwidth: 150 – 9600 MTPS
LLC size: 256KB – 4 MB
Number of prefetchers at different cache level
Notes: using a wide rage of workloads and system configurations

## Slide 19
Trace-driven simulation
using ChampSim
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
SPP [Kim+, MICRO’16]
Bingo [Bakshalipour+, HPCA’19]
MLOP [Shakerinava+, DPC3’19]
SPP+DSPatch [Bera+, MICRO’19]
SPP+ PPF [Bhatia+, ISCA’20]
Wide range of prefetchers
Wide range of system-configurations
150 single-core workloads from SPEC CPU 2006, 2017, PARSEC, and Ligra
270 multi-core workload mixes
Wide range of workloads
#cores: 1 – 12 cores
Main memory bandwidth: 150 – 9600 MTPS
LLC size: 256KB – 4 MB
Number of prefetchers at different cache level
Open-sourced and artifact-evaluated
with all three ACM badges
Notes: Our evaluation infrastructure is fully-open sourced and artifact-evaluated

## Slide 20: Key Results
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Chart: Number of cores
| 1 | 2 | 4 | 6 | 8 | 12
SPP | 1.1809 | 1.2748 | 1.2361 | 1.2322 | 1.2107 | 1.1844
Bingo | 1.1861 | 1.2832 | 1.2186 | 1.1864 | 1.1783 | 1.1578
MLOP | 1.1902 | 1.2833 | 1.2429 | 1.231 | 1.2074 | 1.1769
Pythia | 1.2242 | 1.3243 | 1.3009 | 1.2853 | 1.2704 | 1.2538
SPP
MLOP
Bingo
Pythia
Outperforms prior prefetchers
in wide range of configurations varying core count
Notes: Our evaluation shows that Pythia consistently outperforms multiple
prior state-of-the-art prefetchers
both in single-core and numerous multi-core configurations

## Slide 21: Key Results
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Outperforms prior prefetchers
in wide range of memory bandwidth configurations
Chart: DRAM MTPS (in log scale)
| 150 | 300 | 600 | 1200 | 2400 | 4800 | 9600
SPP | 0.97243 | 1.0879 | 1.1469 | 1.1722 | 1.1809 | 1.183 | 1.1839
Bingo | 0.80726 | 0.93831 | 1.052 | 1.1432 | 1.1861 | 1.199 | 1.2005
MLOP | 0.84028 | 0.99928 | 1.1044 | 1.1689 | 1.1902 | 1.196 | 1.1975
Pythia | 1.009 | 1.1308 | 1.1837 | 1.2142 | 1.2242 | 1.2265 | 1.2278
SPP
MLOP
Bingo
Pythia
Notes: Pythia also outperforms prior prefetchers across
a wide range of memory bandwidth configurations

## Slide 22: Key Results
More performance gains
with customization
Uto 7.8% perf. gain than baseline Pythia in Ligra
by reward customization
Low-overhead, low-latency, and high-throughput predictions
1.03% area and 0.4% power overhead
Meets latency and throughput of an L2 prefetcher
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Moreover, Pythia can be customized in silicon to provide further performance gains than baseline Pythia
[CLICK] and Pythia’s hardware architecture provides low-overhead ...

## Slide 23: Does Pythia Solve the Memory Bottleneck?
# demand loads going to off-chip without Pythia
~50%
successfully prefetched
by Pythia
~50%
still going off-chip
even with Pythia
What to do with these loads
that are still going off-chip?
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Does this mean Pythia solve memory bottleneck?
The answer is no.
If we look into the loads that would have gone to off-chip main memory without Pythia,
we see that nearly half of them are successfully prefetched by Pythia.
[CLICK] but the remaining half are still going to off-chip.
[CLICK] So what to do with these loads that are still going off-chip?

## Slide 24: Key Contributions
Fetch & Decode
Execute
Access Memory
Commit
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Hermes [MICRO’22]
Off-chip prediction (OCP)
using perceptron learning
Athena [under review]
Prefetcher-OCP coordination
using reinforcement learning
Constable [ISCA’24]
Safely eliminating load instruction execution
by exploiting load address-value stability
Pythia [MICRO’21]
Hardware data prefetching
using reinforcement learning
Notes: That brings us to our second contribution -- Hermes.

## Slide 25: Key Observation for Off-Chip Loads
On-chip cache access latency
significantly contributes to the off-chip load latency
40% of the stalls can be eliminated by removing
on-chip cache access latency from critical path
L1
L2
LLC
Main Memory
Saved cycles
L1
L2
LLC
Main Memory
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: In this work, we observe that, on-chip cache access latency ...
[CLICK] 40% of the stalls cycles caused by an off-chip load can be ...

## Slide 26: Our Goal
Improve processor performance
by removing on-chip cache access latency
from the critical path of off-chip loads
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Thus, our goal in this work is to improve ...

## Slide 27
L1
L2
LLC
Main Memory
L1
L2
LLC
Main Memory
Predicts which loads are likely to go off-chip
Starts fetching data directly from main memory
while concurrently accessing the cache hierarchy
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Towards this we propose Hermes, which is based on two key ideas...
[CLICK] First, Hermes predicts which ... early in the pipeline
[CLICK] Second, for those predicted off-chip requests, Hermes starts fetching ...
[CLICK] while also concurrently ...
[CLICK] By doing so, Hermes hides the on-chip cache access latency
under the shadow of main memory access latency
[CLICK] which in turn provides significant performance improvement

## Slide 28
Predicts which loads are likely to go off-chip
The first perceptron-based off-chip load predictor
Adaptively learns to identify off-chip loads from multiple program features
Load Request
Σ
Feature
(e.g., PC)
Trainable weights
Off-chip
prediction
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: To predict which loads are likely to go off-chip, Hermes employs the
first perceptron-based off-chip load predictor that adaptively learns ....
From a given demand request, Hermes extracts a set of program features to retrive

## Slide 29: Trace-Driven Simulation Methodology
Pythia [Bera+, MICRO’21]
Bingo [Bakshalipour+, HPCA’19]
MLOP [Shakerinava+, DPC3’19]
SPP+ PPF [Bhatia+, ISCA’20]
SMS [Somogyi+, ISCA’06]
Prefetchers
110 single-core workloads from SPEC CPU 2006, 2017, PARSEC, and Ligra, and more
220 four-core and eight-core workload mixes
Workloads
History-based predictor [Yoaz+, ISCA’99]
Address Tag-Tracking based predictor
Ideal off-chip predictor
Off-chip Predictors
# cores: 1- 8 cores
Main memory bandwidth: 200-12800 MTPS
Cache access latency
Interconnect latency
...
System Configurations
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]

## Slide 30: Trace-Driven Simulation Methodology
Pythia [Bera+, MICRO’21]
Bingo [Bakshalipour+, HPCA’19]
MLOP [Shakerinava+, DPC3’19]
SPP+ PPF [Bhatia+, ISCA’20]
SMS [Somogyi+, ISCA’06]
Prefetchers
110 single-core workloads from SPEC CPU 2006, 2017, PARSEC, and Ligra, and more
220 four-core and eight-core workload mixes
Workloads
History-based predictor [Yoaz+, ISCA’99]
Address Tag-Tracking based predictor
Ideal off-chip predictor
Off-chip Predictors
# cores: 1- 8 cores
Main memory bandwidth: 200-12800 MTPS
Cache access latency
Interconnect latency
...
System Configurations
Open-sourced and artifact-evaluated
with all three ACM badges
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]

## Slide 31: Key Results
Chart: Geomean speedup over no-prefetching
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | GEOMEAN
Hermes | 1.0966 | 1.1185 | 1.1061 | 1.1108 | 1.1309 | 1.115
Pythia | 1.2123 | 1.2715 | 1.0568 | 1.1992 | 1.2108 | 1.2034
Pythia + Hermes | 1.2628 | 1.3007 | 1.1279 | 1.2388 | 1.2854 | 1.2574
Provides performance gains by itself
and when added on top of sophisticated prefetchers
11.5%
5.4%
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]

## Slide 32: Key Results
High-accuracy and high-coverage
Off-chip prediction with 77% accuracy & 74% coverage
Low storage and
low power overhead
Only 4 KB storage per core
1.5% increase in power over Pythia
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Our simulation-based evaluation shows that Hermes provides ...
[CLICK] Hermes improves performance by itself, and also when added on top of ...
[CLICK] And Hermes’s performance benefits come at a modest overhead in storage and power consumption

## Slide 33: One Problem: Two Fundamentally-Different Approaches
Predicts address
of future memory requests
Data prefetcher
Predicts whether or not a given memory request would go off-chip
Off-chip predictor
How do they behave together?
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: With that, we proposed two fundamentally-different speculative mechanisms
targeted towards the same memory bottleneck problem:
[CLICK] Pythia addresses memory bottleneck by predicting future memory addresses
[CLICK] whereas, Hermes addresses memory bottleneck by predicting which memory requests would go off-chip
Technically, these two techniques can be applied together in a system.
But then the question is [CLICK] how do they ...

## Slide 34: Key Contributions
Fetch & Decode
Execute
Access Memory
Commit
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Hermes [MICRO’22]
Off-chip prediction (OCP)
using perceptron learning
Athena [under review]
Prefetcher-OCP coordination
using reinforcement learning
Constable [ISCA’24]
Safely eliminating load instruction execution
by exploiting load address-value stability
Pythia [MICRO’21]
Hardware data prefetching
using reinforcement learning
Notes: This brings us to the third contribution of this thesis – Athena.

## Slide 35: Key Observations
Off-chip prediction (OCP) and data prefetching individually provide complementary performance gains
Especially in memory bandwidth-constrained systems, where prefetcher
often degrades performance, but an OCP improves performance
Naively combination is not beneficial
Enabling both mechanisms often negates performance benefits of OCP
Existing mechanisms lack flexibility or have significant performance headroom
TLP [Jamet+, HPCA’24] lacks flexibility.
HPAC [Ebrahimi+, MICRO’09] and MAB [Gerogiannis+, MICRO’23] are not optimal
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: In this work, we observe that ...
[CLICK] off-chip prediction is a viable alternative ...
especially in memory ...
[CLICK] Yet, naively combining both of these mechanisms is not beneficial,
especially in bandwidth-constrained systems, where enabling both mechanism often negates ...
[CLICK] and existing coordination mechanism either lack flexibility
in a sense that they cannot coordinate an off-chip predictor
in presence of multiple prefetchers scattered throughout the cache hierarchy,
or they leave a substantial room for performance improvement behind

## Slide 36: Our Goal
Design a holistic framework that
Autonomously synergizes OCP with
multiple prefetchers throughout the cache hierarchy
To deliver consistent performance benefits,
regardless of workloads and system configuration
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Thus, our goal in this work is to design ...
autonomously ...
to deliver ...

## Slide 37
Key Idea: Formulate OCP-prefetcher coordination
as a reinforcement learning problem
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Towards this, we propose Athena, whose key idea is to ...

## Slide 38
Athena
Processor and Memory System
RL agent
Environment
Autonomously learn
how to coordinate
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Athena itself acts as the RL agent whose
[CLICK] goal is to autonomously ...
[CLICK] by interacting with the environment which is ...

## Slide 39
Athena
Processor and Memory System
Statet
Actiont
Rewardt
System features
(e.g., b/w usage, prefetcher accuracy)
Coordination action
(i.e., what to enable
& how much to enable)
Change in telemetry
(e.g., IPC, #LLC miss, #load instructions)
t = N committed instructions
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: At the end of every epoch, which is a fixed number of committed instructions ...
[CLICK] Athena extracts a set of system-level features such as ..
and use it as a state information
[CLICK] to take a coordination action. An action in this case is
not only to determine which mechanism to enable, but also how much aggressiveness a mechanism should be enabled with.
[CLICK] At the end of the epoch, the environment provides a numerical reward to Athena
that incorporates the change in system-level telemetry, that are directly affected by Athena’s actions (such as change in IPC),
but also, telemetry that are seemingly uncorrelated to Athena’s action (such as change in number of load instructions).
[This is to ensure that Athena not only learns from the impact of its own actions,
but also from the change in the program phase behavior.]

## Slide 40: Trace-Driven Simulation Methodology
Stride [Baer, SC’91]
IPCP [Pakalapati+, ISCA’20]
Pythia [Bera+, MICRO’21]
SPP+ PPF [Bhatia+, ISCA’20]
SMS [Somogyi+, ISCA’06]
MLOP [Shakerinava+, DPC3’19]
Prefetchers
100 single-core workloads
180 four-core and eight-core workload mixes
Workloads
Hermes [Bera+, MICRO’22]
HMP [Yoaz+, ISCA’99]
TTP [Jalili+, HPCA’22]
Off-chip Predictors
# cores: 1- 8 cores
Main memory bandwidth: 200 - 1600 MTPS
4 cache designs with various prefetchers at different cache levels
System Configurations
HPAC [Ebrahimi+, MICRO’09]
MAB [Yoaz+, ISCA’99]
TLP [Jamet+, HPCA’24]
Coordination Policies
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: We evaluate Athena in coordinating multiple types of prefetcher and off-chip predictors
under a wide range of workloads and system configurations

## Slide 41: Key Results
Chart: Speedup
| SPEC | PARSEC | Ligra | CVP | All
Naive | 0.99982 | 1.0183 | 1.0304 | 1.1667 | 1.0457
Best-prior policy | 1.0138 | 1.0216 | 1.0196 | 1.1702 | 1.0527
Athena | 1.0654 | 1.0872 | 1.041 | 1.2376 | 1.1056
Chart: Speedup
| SPEC | PARSEC | Ligra | CVP | All
Naive | 1.1097 | 0.87993 | 1.0253 | 1.2391 | 1.093
Best-prior policy | 1.0862 | 0.90302 | 1.0268 | 1.2248 | 1.0833
Athena | 1.0993 | 1.0857 | 1.0467 | 1.2869 | 1.1355
Chart: Speedup
| SPEC | PARSEC | Ligra | CVP | All
Naive | 1.0012 | 1.0184 | 1.0303 | 1.1728 | 1.0478
Best-prior policy | 1.0331 | 1.0305 | 1.0306 | 1.196 | 1.0709
Athena | 1.0673 | 1.0828 | 1.04 | 1.2563 | 1.11
Chart: Speedup
| SPEC | PARSEC | Ligra | CVP | All
Naive | 0.98105 | 0.79534 | 1.0126 | 1.034 | 0.97126
Best-prior policy | 1.0292 | 0.96166 | 1.0257 | 1.1594 | 1.0505
Athena | 1.0816 | 1.0947 | 1.0482 | 1.2739 | 1.1239
OCP + 2 prefetchers @ L2
OCP + 1 prefetcher @ L1 & L2
OCP + 1 prefetcher @ L2
OCP + 1 prefetcher @ L1
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Our evaluation shows that, across a wide range of system configuration
with different number of prefetchers at different cache levels
[CLICK] Consistently outperforms [CLICK] in all system configurations

## Slide 42: Key Results
Consistent performance benefit
In coordinating four types of prefetchers
and three types of off-chip predictors
Low storage overhead
Only 3 KB per core
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Moreover, Athena provides consistent performance benefit ...
[CLICK] all while incurring a modest storage overhead.

## Slide 43: Key Contributions: Recap
Fetch & Decode
Execute
Access Memory
Commit
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Hermes [MICRO’22]
Off-chip prediction (OCP)
using perceptron learning
Athena [under review]
Prefetcher-OCP coordination
using reinforcement learning
Constable [ISCA’24]
Safely eliminating load instruction execution
by exploiting load address-value stability
Pythia [MICRO’21]
Hardware data prefetching
using reinforcement learning
Notes: With that, we look three proposals in this thesis,
[CLICK] Pythia, Hermes, and Athena - all of which aim to alleviate memory bottleneck
[CLICK] by finding inefficiencies at the memory hierarchy level

## Slide 44: Key Contributions
Fetch & Decode
Execute
Access Memory
Commit
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Hermes [MICRO’22]
Off-chip prediction (OCP)
using perceptron learning
Athena [under review]
Prefetcher-OCP coordination
using reinforcement learning
Constable [ISCA’24]
Safely eliminating load instruction execution
by exploiting load address-value stability
Pythia [MICRO’21]
Hardware data prefetching
using reinforcement learning
Notes: But inefficiencies also arise inside the core’s execution.
Addressing these inefficiencies can also help in alleviating memory bottleneck.
That brings us to our fourth contribution – Constable

## Slide 45: Key Observations
A large fraction (34%) of dynamic loads fetch
the same data from the same address
throughout the entire workload
Techniques like load value prediction (LVP) and memory renaming (MRN)
do not fully exploit this data characteristic
These loads cause instruction-level parallelism loss due to resource dependence
i.e., blocking other loads from getting executed due to limited resources.
LVP and MRN fail to mitigate resource dependence
Mitigating both data and resource dependence has higher potential performance improvement
Eliminating execution of such loads provides more than 2X potential performance benefit than just breaking their data dependence
2X
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: In this work we observe that
[CLICK] a large fraction of load instructions executed by the processor infact fetches ...
prior techniques like ... do not fully exploit this data characteristics ...
[CLICK] We show that these loads cause significant loss in instruction-level parallelism
due to sheer resource dependence even in presence of sophisticated techniques like LVP and MRN
[CLICK] Mitigating both the data and resource dependence on these loads ...
has double potential performance benefit than just breaking their data dependence.

## Slide 46: Our Goal
Improve instruction-level parallelism by
mitigating both load data and resource dependence
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Thus our goal in this work is to ...

## Slide 47: Constable: Key Insight
mov r8, [rbp+0x8]
sub rax, r8
cmp rsi, rax
jle 0x40230e
add rax, 0x10
mov r8, [rbp+0x8]
sub rax, r8
cmp rsi, rax
jle 0x40230e
Dynamic instruction stream
add rax, 0x10
add rax, 0x10
Two successive dynamic instances
of the same static load instruction
LD1
LD2
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Towards this we propose Constable,
which is based on a simple key insight that if there are two successive dynamic instances
X1 and X2 of a load instruction,
[CLICK] then X2 will fetch... if:
[CLICK] None of the ...
[CLICK] No store or snoop ...

## Slide 48: Constable: Key Insight
If the source register (rbp)
has not been modified
mov r8, [rbp+0x8]
sub rax, r8
cmp rsi, rax
jle 0x40230e
add rax, 0x10
mov r8, [rbp+0x8]
sub rax, r8
cmp rsi, rax
jle 0x40230e
Dynamic instruction stream
add rax, 0x10
add rax, 0x10
LD2 would have the same address as LD1
Address generation of LD2
can be eliminated
If no store or snoop request
to address [rbp+0x8]
LD2 would fetch the same data as LD1
Data fetching of LD2
can be eliminated
LD1
LD2
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Constable is based on a simple key insight that if there are two successive dynamic instances
X1 and X2 of a load instruction,
[CLICK] then X2 will fetch... if:
[CLICK] None of the ...
[CLICK] No store or snoop ...

## Slide 49: Constable: Key Steps
Dynamically identify load instructions
that have historically fetched
the same data from the same load address
(i.e., likely-stable)
Eliminate execution of likely-stable loads
by tracking modifications to
their source registers and their load addresses
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Notes: Based on this insight, Constable works on two key steps:
[CLICK] First, Constable dynamically identifies ...
[CLICK] For every likely-stable load, Constable tracks modifications ...
[CLICK] and eliminates their execution until there is a write ...

## Slide 50: Evaluation with Industry-Grade Simulator
Aggressive OoO processor
With memory renaming, zero/constant/move elimination, branch folding
Five data prefetchers
Strong Baseline
90 workloads from variety of application domains
  SPEC CPU 2017
  Client
  Enterprise
  Server
Workloads
EVES, the state-of-the-art load value predictor [Seznec+, CVP’18]
Early load address resolution [Berkerman+, ISCA’00]
Register file prefetching [Shukla+, ISCA’22]
Compared Against
Without simultaneous multithreading
With 2-way simultaneous multithreading
System Configurations
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]

## Slide 51: Key Results – Without SMT
Chart: Speedup
| Client | Enterprise | FSPEC17 | ISPEC17 | Server | GEOMEAN
EVES | 1.1038 | 1.0884 | 1.009 | 1.0215 | 1.0304 | 1.0474
Constable | 1.0386 | 1.0858 | 1.0545 | 1.0148 | 1.0607 | 1.0514
EVES+Constable | 1.1289 | 1.1223 | 1.0518 | 1.0289 | 1.0947 | 1.0854
5.1%
3.4%
Provides performance gains by itself
and when added on top of load value predictor
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]

## Slide 52: Key Results – With 2-way SMT
Higher performance benefits
in a 2-way SMT processor
Chart: Speedup
| Client | Enterprise | FSPEC17 | ISPEC17 | Server | GEOMEAN
EVES | 1.0794 | 1.0762 | 1 | 1.0048 | 1.0157 | 1.0355
Constable | 1.0624 | 1.0968 | 1.1166 | 1.0058 | 1.1175 | 1.088
EVES+Constable | 1.1316 | 1.1332 | 1.1124 | 1.0116 | 1.1294 | 1.1133
8.8%
11.3%
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]

## Slide 53: Key Results
Improved resource efficiency
26% L1-D access reduction,
8.8% RS allocation reduction
Low storage and area overhead
12.4 KB per core, 0.232 mm2 area overhead
Athena [under review]
Pythia [MICRO’21]
Hermes [MICRO’22]
Constable [ISCA’24]
Reduction in dynamic power
9.1% L1-D power reduction, 5.1% RS power reduction
Notes: Our extensive evaluation with an industry-grade simulator shows that:
[CLICK] Constable provides ... over a SOTA processor that already employs
the SOTA LVP and memory renaming ... both in no SMT ...
[CLICK] On top of improving performance, Constable also improves ...
which in turn reduces the dynamic power consumption of the system...
[CLICK] all while incurring a modest storage and area overhead ...

## Slide 54: Putting It All Together
Notes: To put together everything that we have discussed till now...

## Slide 55: Recall: Thesis Statement
Adapt its policies by continuously learning
from application data and system-generated data
Tailor its decisions by exploiting characteristics
of application data
By enabling microarchitecture to
We can significantly improve performance and
energy efficiency of state-of-the-art processors
Notes: We started with a hypothesis that by enabling microarchitecture ...

## Slide 56: Key Contributions
Fetch & Decode
Execute
Access Memory
Commit
Hermes [MICRO’22]
Off-chip prediction (OCP)
using perceptron learning
Athena [under review]
Prefetcher-OCP coordination
using reinforcement learning
Constable [ISCA’24]
Safely eliminating load instruction execution
by exploiting load address-value stability
Pythia [MICRO’21]
Hardware data prefetching
using reinforcement learning
Notes: [CLICK] First, we propose Pythia, a RL based hardware data prefetcher
[CLICK] Second, we propose Hermes, a perceptron-learning-based off-chip load prediction mechanism
[CLICK] Third, we propose Athena, a RL-based approach to coordinate prefetching and off-chip prediction
[CLICK] Fourth, we propose Constable, a safe load execution elimination technique by exploiting load instruction characteristics

## Slide 57: Putting it All Together
Hermes [MICRO’22]
Off-chip prediction (OCP)
using perceptron learning
Athena [under review]
Prefetcher-OCP coordination
using reinforcement learning
Constable [ISCA’24]
Safely eliminating load instruction execution
by exploiting load address-value stability
ML-driven techniques
Data-aware technique
Adapt their policies by continuously learning
from application data and system-generated data
Tailor its decisions by exploiting characteristics
of the application data
Pythia [MICRO’21]
Hardware data prefetching
using reinforcement learning
Notes: where Pythia, Hermes, and Athena in unison exemplifies techniques
that uses machine learning to adapt ...
whereas Constable exemplifies technique that exploits
new data characteristics to tailor microarchitectural decisions

## Slide 58: Putting it All Together
Hermes [MICRO’22]
Off-chip prediction (OCP)
using perceptron learning
Athena [under review]
Prefetcher-OCP coordination
using reinforcement learning
Constable [ISCA’24]
Safely eliminating load instruction execution
by exploiting load address-value stability
Significantly improve
performance and/or energy efficiency
over best-prior mechanisms
Pythia [MICRO’21]
Hardware data prefetching
using reinforcement learning
Notes: All four techniques significantly improve
the performance and/or energy efficiency over their respective SOTA mechanisms,
thus, quantitatively substantiating the central statement of the thesis.

## Slide 59: Recall: Thesis Statement
Adapt its policies by continuously learning
from application data and system-generated data
Tailor its decisions by exploiting characteristics
of application data
By enabling microarchitecture to
We can significantly improve performance and
energy efficiency of state-of-the-art processors
Notes: We started with a hypothesis that by enabling microarchitecture ...

## Slide 60: Future Directions
RL-driven online instruction criticality prediction
RL-driven shared resource partitioning in multi-core systems
Multi-agent RL for coordinated caching, prefetching & memory scheduling
Compiler-microarchitecture co-design to eliminate redundant loads
Near-accurate speculation-aware lazy instruction execution
Extend
Off-chip prediction in GPUs/accelerators
Accurate memory location prediction for disaggregated memory systems
Off-chip prediction for transparent identification of PIM regions
Learning-based data partitioning/placement for PIM
Learning-based self-adaptive prefetcher for PIM
Expand
Notes: That said, the ML-driven and data-aware design principles advocated in this thesis
can be extended to many other microarchitectural decision making beyond what we have demonstrated.
[CLICK] We can extend these principles to other mechanisms employed in general-purpose processors, such as ...
[CLICK] The same design principles can also be expanded beyond general-purpose processors, such as ...

## Slide 61: My Involvements During Ph.D.
2019
2020
2021
2022
2023
2024
2025
Thesis
publications
Bera+
MICRO’21
Bera+
MICRO’22
Bera+
ISCA’24
Lang & Bera+
under review
Other major
contributions
Bera+
MICRO’19
Nori+
ISCA’21
ML-driven
storage system
Singh+
ISCA’22
Nadig+
arXiv’25
Address
translation system
Kanellopoulos+
MICRO’23
Kanellopoulos+
ASPLOS’25
Near data
processing
Denzler+
IEEE Access’23
Kabra+
ASPLOS’25
Energy-efficient
architecture
Olgun+
TACO’24
Haj-Yahya+
MICRO’21
Kanellopoulos+
MICRO’23
Kanellopoulos+
arXiv’25
Notes: This brings me to the last part of the presentation...
I am thankful to contribute to many other interesting projects beyond what contribute to my thesis

## Slide 62: Acknowledgements
Onur Mutlu
Anant V. Nori, Sree Subramoney
Aamer Jaleel, Boris Grot, Chris Wilkerson, Daniel Jiménez, Pradip Bose
Kaveh Razavi
Amazingly-talented mentees: Zhenrong, Sgouras, Clément, and Liana
All SAFARI group members (especially Big K., Nika, Rakesh, and Mohammad)
Industrial partners & sponsors
Friends and colleagues all over the world
My mother, my wife, and my aunt
Notes: This thesis won’t be possible without the help from numerous people, ....

## Slide 63: Acknowledgements
My beloved baba,
Mr. R. R. Bera
(1960 - 2020)
Notes: This thesis won’t be possible without the help from numerous people, ....

## Slide 64: Mitigating the Memory Bottleneck with Machine Learning-Driven and Data-Aware Microarchitectural Techniques
Rahul Bera
Doctoral Examination
01.10.2025
Advisor:
Onur Mutlu (ETH Zurich)
Co-Examiners:
Aamer Jaleel (Nvidia Research)
Boris Grot (University of Edinburgh)
Chris Wilkerson (Intel)
Daniel Jiménez (Texas A&M University)
Pradip Bose (IBM T. J. Watson Research Center)
Notes: This concludes my talk...
I will be happy to take questions...

## Slide 65: Influence on the Community

## Slide 66: Open-Sourced Artifacts

## Slide 67: Impact on the Community
Pythia, Hermes, and Constable – all have served as the state-of-the-art in many subsequent works
MICRO’23
MICRO’23
MICRO’22
MICRO’25
HPCA’24
IISWC’25

## Slide 68: Backup

## Slide 69
Hermes
Athena
Constable
Pythia

## Slide 70: Pythia Discussion

## Slide 71: Pythia Discussions
FAQs
  Why RL?
  What about large page?
  What’s the prefetch degree?
  Can customization happen during workload execution?
  Can runtime mixing create problem?
Simulation and Methodology
  Basic Pythia configuration
  System parameters
  Configuration of prefetchers
  Evaluated workloads
  Feature selection
Detailed Design
  Reward structure
  Design overview
  QVStore Organization
More Results
  Comparison against other adaptive prefetchers
  Comparison against Context prefetcher
  Feature combination sensitivity
  Hyperparameter sensitivity
  Comparison with multi-level prefetchers
  Performance in unseen workloads
  Single-core s-curve
  Four-core s-curve
  Detailed performance analysis
  Benefit of bandwidth awareness
  Case study
  Customizing rewards
  Customizing features

## Slide 72: (1) Single-Feature Prefetch Prediction
Provides good performance gains mainly on workloads where the feature-to-pattern correlation exists
[1] Bakshalipour et al., HPCA’19
[2] Kim et al., MICRO’16
Chart: IPC improvement over baseline (%)
| 482.sphinx3-417B | PARSEC-Canneal | PARSEC-Facesim | 459.GemsFDTD-765B
SPP | 0.25977 | 0.028455 | 0.11952 | 0.38946
Bingo | 0.41337 | 0.063762 | 0.17478 | 0.3437
Pythia | 0.50416 | 0.077957 | 0.17503 | 0.40433
15.4%
3.5%
5.5%
4.6%
Bingo [1] performs better
SPP [2] performs better
Notes: Due to the use of a single program feature for prefetch prediction, a prefetcher typically provides performance benefits …
In other types of workloads, the same prefetcher fails to provide performance gains.
To illustrate this [CLICK], we show the coverage, overprediction, and performance improvement of two prior prefetchers SPP and Bingo for six sample workloads.
The top figure shows …
The bottom figure shows …
As we can see, for workloads like [CLICK], … Bingo performs better than SPP, as the program feature exploited by Bingo has stronger correlation with the access pattern than SPP.
On the other hand, for workloads like … [CLICK], SPP’s program feature provides better correlation, and thus performs better than Bingo.

## Slide 73: (2) Lack of Inherent System Awareness
Little understanding of undesirable effects (e.g., memory bandwidth usage, cache pollution, …)
  Performance loss in resource-constrained configurations
Chart: Fraction of LLC misses
| SPP | Bingo | Pythia | SPP | Bingo | Pythia | Ligra-CC | PARSEC-Canneal
Covered | 0.050822 | 0.22755 | 0.24042 | 0.15097 | 0.27515 | 0.31283
Uncovered | 0.94918 | 0.77245 | 0.75958 | 0.84903 | 0.72485 | 0.68717
Overpredicted | 0.31635 | 2.6825 | 0.57152 | 0.55316 | 4.7397 | 0.27171
Chart: IPC improvement over baseline (%)
| Ligra-CC | PARSEC-Canneal
SPP | 0.028046 | 0.028455
Bingo | -0.018714 | 0.063762
Pythia | 0.069103 | 0.077957
368%
574%
Similar coverage
Lower overpredictions
Yet, lower performance
Notes: The second shortcoming is that, all prior prefetchers have …, which often leads to …
To illustrate this, let revisit the previous figure and focus on Bingo’s performance in PARSEC-Canneal and Ligra-CC.
Bingo in Ligra-CC has similar coverage to PARSEC-Canneal with significantly …
The reason is that, in baseline without prefetching, Ligra-CC consumes much higher main memory …
As a result, even a smaller amount of overprediction hurts more performance in Ligra-CC than in PARSEC-Canneal.
This is only happening as Bingo does not take its undesirable effects into account while prefetching.
Thus the key takeaway is that, [CLICK] …

## Slide 74: (3) Lack of In-silicon Customizability
Feature statically selected at design time
  Rigid hardware designed specifically to exploit that feature
No way to change program feature and/or change prefetcher’s objective in silicon
  Cannot adapt to a wide range of workload demands
Design from scratch
Verify
Fabricate
Notes: The third key shortcoming is that, all prior prefetcher lack in-silicon customizability.
These prefetchers statically selects the feature to exploit at design time and design a rigid hardware to specifically …
[CLICK] There is no way …
In order to exploit a new program feature, architects need to design a prefetcher from scratch …
[CLICK] and this cycle goes on for every new prefetcher. This wastes precious design time and human resource.

## Slide 75: Why RL? Why Not Supervised Learning?
Determining the benefits of prefetching (i.e., whether a decision was good for performance or not) is not easy
  Depends on a complex set of metrics
    Coverage, accuracy, timeliness
    Effects on system: b/w usage, pollution, cross-application interference, …
  Dynamically-changing environmental conditions change the benefit
  Delayed feedback due to long latency (might not receive feedback at all for inaccurate prefetches!)
Differs from classification tasks (e.g., branch prediction)
  Performance strongly correlates mainly to accuracy
  Does not typically depend on environment
  Bounded feedback delay

## Slide 76: What About Large Pages?
Pythia’s framework can be easily extended to incorporate additional prefetch actions (i.e., possible prefetch offsets for the page size)
To decrease the storage overhead
  Prune action space via automatic design-space exploration
  Hash action values to retrieve Q-values

## Slide 77: What is the Prefetch Degree? Is It Managed by the RL Agent?
Pythia employs a simple degree selector, separate from the RL agent
  If the agent has selected the same prefetch action (O) multiple times in a row, Pythia increases the degree (A+2O, A+3O, …)
  At most degree 4
Future works on managing degree by the RL agent

## Slide 78: Can the Customization Be Done While the Workload is Running?
Certainly.
Pythia, being an online learning technique, will autonomously adapt (and optimize) its policy to use the new program features or the modified reward values

## Slide 79: Can Runtime Workload Mix Create an Issue?
We implement the bandwidth usage feedback using a counter in the memory controller. Thus Pythia already has a global view of the memory bandwidth usage that incorporates all workloads running on a multi-core system
We evaluate a diverse set (300 of each category) of four-core, eight-core, twelve-core random workload mixes
Based on our evaluation, we observe that Pythia dynamically adapts itself to varying workload demands

## Slide 80: How does Pythia Compare Against Other Adaptive Prefetching Solutions?
We compare Pythia against IBM POWER7[5] prefetcher
  Adaptively selects prefetcher degree/configuration by monitoring program IPC
Chart: Geomean speedup over baseline
| SPEC06 | SPEC17 | PARSEC | Ligra | Cloudsuite | GEOMEAN
POWER7 | 1.3317 | 1.175 | 1.1506 | 1.2944 | 1.0365 | 1.1789
Pythia | 1.4369 | 1.2569 | 1.2326 | 1.3254 | 1.0485 | 1.2242
Chart: Geomean speedup over baseline
| SPEC06 | SPEC17 | PARSEC | Ligra | Cloudsuite | Mix | GEOMEAN
POWER7 | 1.2873 | 1.1382 | 1.1343 | 1.2931 | 1.0386 | 1.3155 | 1.2345
Pythia | 1.3786 | 1.2234 | 1.2156 | 1.3212 | 1.0507 | 1.4086 | 1.299
(a) single-core
(b) four-core
4.5%
6.4%
[5] Jimenez et al., TOPC’14

## Slide 81: How Does Pythia Compare Against the Context Prefetcher?
Pythia widely differs from the Context Prefetcher (CP)[6] in all three aspects: state, action, and reward. The key differences are:
  CP does not consider system-level feedback
  CP models the agent as a contextual bandit which takes myopic prefetch decisions as compared to Pythia
  CP requires compiler support to extract software-level features
Pythia outperforms CP-HW by 5.3% in single-core and 7.6% in four-core system
[6] Leeor et al., ISCA’15

## Slide 82: How Pythia’s Performance Changes With Various State Definitions You Have Swept?
In total we evaluate state defined as any-one, any-two, and any-three combinations of 32 features
Performance gain ranges from 20.7% to 22.4%
Coverage ranges from 66.2% to 71.5%
Overprediction ranges from 26.7% to 32.2%

## Slide 83: Is Pythia Sensitive to Hyperparameter?
Not setting hyperparameters can significantly impact the overall performance improvement
Changing 𝜀 from 0.002 to 1.0 drops perf. by 16%
Changing 𝛼 from 0.0065 to 1.0 drops perf. by 5.4%

## Slide 84: How Does Pythia Compare Against Commercial Multi-level Prefetchers?
Chart: DRAM MTPS (in log scale)
| 150 | 300 | 600 | 1200 | 2400 | 4800 | 9600
Stride-L1+Streamer-L2 | 0.9366 | 1.083 | 1.1579 | 1.1975 | 1.2105 | 1.2136 | 1.2152
IPCP | 0.85928 | 1.0124 | 1.121 | 1.1951 | 1.2213 | 1.2285 | 1.2301
Stride-L1+Pythia-L2 | 1.0014 | 1.1296 | 1.1873 | 1.2214 | 1.2341 | 1.2376 | 1.2386
Pythia outperforms IPCP [7] by 14.2% on average in 150-MTPS
[6] Prakalapati et al., ISCA’20

## Slide 85: Does Pythia Perform Equally Well for Unseen Workloads also?
Evaluated with 500 traces from value prediction championship
  No prefetcher has been trained on these traces
Pythia outperforms MLOP and Bingo by
8.3% and 3.5% in single-core
And 9.7% and 5.4% in four-core

## Slide 86: Basic Pythia Configuration

## Slide 87: System Parameters

## Slide 88: Configuration of Prefetchers

## Slide 89: Evaluated Workloads

## Slide 90: List of Evaluated Features

## Slide 91: Performance S-curve: Single-core
Chart: Workload number
623.xalancbmk_s-592B
603.bwaves_s-2931B
462.libquantum
streamcluster
429.mcf
BFSCC-22B
pagerank-51B
fluidanimate-9500M

## Slide 92: Performance S-curve: Four-core
Chart: Workload number
429.mcf-184B
pagerank
462.libquantum-1343B
437.leslie3d-271B
Mix-59
raytrace-23.75B
Mix-240

## Slide 93: Single-core Coverage & Overprediction

## Slide 94: Detailed Performance

## Slide 95: Benefit of Bandwidth Awareness
Chart: DRAM MTPS (in log scale)
| 150 | 300 | 600 | 1200 | 2400 | 4800 | 9600
Memory BW-oblivious Pythia | -0.046299 | -0.024802 | -0.012489 | -0.0039965 | -0.0026675 | -0.0019809 | -0.0020878

## Slide 96: Case Study

## Slide 97: Customizing Rewards

## Slide 98: Customizing Features

## Slide 99: Hermes Discussions

## Slide 100: Hermes Discussions
FAQs
  What are the selected set of program features?
  Can you provide some intuition on why these features work?
  What happens in case of a misprediction?
  What’s the performance headroom for off-chip prediction?
  Do you see a variance of different features in final prediction accuracy?
Simulation Methodology
  System parameters
  Evaluated workloads
More Results
  Percentage of off-chip requests
  Reduction in stall cycles by reducing the critical path
  Fraction of off-chip load requests
  Accuracy and coverage of POPET
  Effect of different features
  Are all features required?
  1C performance
  1C performance line graph
  1C performance against prior predictors
  Effect on stall cycles
  8C performance
  Sensitivity:
    Hermes request issue latency
    Cache hierarchy access latency
    Activation threshold
    ROB size
    LLC size
  Power overhead
  Accuracy without prefetcher
  Main memory request overhead with different prefetchers

## Slide 101: Hermes Overview
Core
L1-D
L2
LLC
MC
Off-Chip
Main Memory
L1
L2
LLC
Main Memory
Baseline
Processor is stalled
Latency tolerance limit of ROB
Notes: Now let me give you a brief overview of Hermes.
This is how a traditional cache hierarchy looks like in today’s processor.
[CLICK] And this is how the memory latency timeline looks like for an off-chip load in the baseline system
[CLICK] If the ROB has a latency tolerance limit up till here, the processor stalls for the remaining cycles

## Slide 102: Hermes Overview
Core
L1-D
L2
LLC
MC
Off-Chip
Main Memory
L1
L2
LLC
Main Memory
POPET
L1
L2
LLC
Main Memory
Baseline
Hermes
Saved stall cycles
Processor is stalled
Latency tolerance limit of ROB
Predict
Issue a Hermes request
Wait
Train
Perceptron-based
off-chip load predictor
Notes: Now Hermes employs an off-chip predictor named POPET.
[CLICK] For every load generated in the core, Hermes consults POPET to predict whether this load would go off-chip or not
[CLICK] If the load is predicted to go off-chip, Hermes waits for the address translation to finish, which happens in parallel with L1 cache access
[CLICK] And then issues a speculative memory request, which we call a Hermes request,
directly to the main memory controller to start fetching the data from the main memory,
While also concurrently accessing the cache hierarchy for such a load.
[CLICK] If the off-chip prediction is correct, the load would eventually miss the LLC and arrive at the memory controller
Where it will simply wait for the ongoing Hermes request to finish, thus hiding the entire cache access latency from its critical path.
Once the data returns from the main memory, Hermes returns the data to the core [CLICK],
Thus, saving the precious stall cycles induced by the off-chip load [CLICK], which in turn provides performance benefit.
[CLICK] Hermes trains POPET when the data finally returns to the core, closing the feedback loop.

## Slide 103: Designing the Off-Chip Load Predictor
Tracking cache contents
Learning from program behavior
  Large metadata
  Metadata size increases with cache hierarchy size
  May need to track all cache operations
  Gets complex depending on the cache hierarchy configuration (e.g., inclusivity, bypassing,…)
  Correlate different program features with off-chip loads
MissMap [Loh+, MICRO’11] for the DRAM cache,
D2D [Sembrant+, ISCA’14], D2M [Sembrant+, HPCA’17], LP [Jalili+, HPCA’22] for the cache hierarchy
History-based prediction
HMP [Yoaz+, ISCA’99] for the L1-D cache
Using branch-predictor-like hybrid predictor:
Global, Gshare, and GSkew
Low storage overhead
Low design complexity
POPET provides
both higher accuracy and higher performance
than predictors inspired from these previous works
Notes: Now let’s discuss how to design this off-chip predictor.
So, there are multiple prior works that can be used either directly or with small modifications for off-chip load prediction.
These works can be broadly categorized into two classes.
[CLICK] History-based predictor introduced by HMP, uses a branch-predictor like hybrid predictor design
to identify which requests are going to miss L1 cache.
We can easily extend HMP’s design to predict loads that are going to miss the entire cache hierarchy.
[CLICK] Tracking-based methods, on the other hand, explicitly track cache contents
to predict which load requests are going to miss the cache hierarchy.
[CLICK] These tracking-based methods poses two key challenges…
[CLICK] First,…
[CLICK] Second,…
[CLICK] POPET takes a completely different approach to predict off-chip load requests by learning from program behavior.
[CLICK] It aims to correlate multiple different types of program features with off-chip load requests
to provide accurate predictions with much lower storage overhead and design complexity.
[CLICK] In our paper, we compare POPET against predictors inspired from these prior works and show that
[CLICK] POPET provides both higher accuracy and performance than them.

## Slide 104: POPET: Perceptron-Based Off-Chip Predictor
Multi-feature hashed perceptron model[1]
  Each feature has its own weight table
    Stores correlation between feature value and off-chip prediction
[1] D. Tarjan and K. Skadron, “Merging Path and Gshare Indexing in Perceptron Branch Prediction,” TACO, 2005
Notes: Now let’s deep dive into our off-chip predictor design.
Our predictor, named as POPET, is designed using hashed-perceptron model.
[CLICK] where each feature has its own weight table
That stores the correlation between feature value and the off-chip prediction

## Slide 105: Predicting using POPET
Uses simple table lookups, addition, and comparison
0x7ffe0+12
42
-4
12
3
3 >= -2
-5
Predict that the load would go off-chip
Extract features from the load request
Notes: Hermes predicts using POPET using simple operations like table lookup, addition, and comparison.
Let me give you an example on how POPET’s prediction works.
POPET’s prediction works in three stages.
[CLICK] In the first stage, POPET extracts the features from the load request
[CLICK] In the second stage, each feature value is hashed and used as an index to retrieve the weights from each individual weight tables
[CLICK] In the third stage, the retrieved weights are accumulated and the cumulative weight is used to compute the activation function.
[CLICK] If the cumulative weight is higher than the activation threshold, POPET predicts that the load would go off-chip.

## Slide 106: Training POPET
Uses simple increment or decrement of feature weights
0x7ffe0+12
42
-4
12
3
3 >= -2
-5
Predict that the load would go off-chip
Shouldn’t be activated
Cumulative weight < 𝜏act
-1
-1
-1
Notes: Now let’s understand how to train POPET.
For this let’s assume the previous example where the load is predicted to go off-chip.
[CLICK] But in reality, the load didn’t go off-chip
[CLICK] this means the activation which have triggered before, shouldn’t have triggered
Which means, the cumulative weight should be lower than the activation threshold
[CLICK] Now to adjust the feature weights, POPET again indexes each weight table using the hashed feature values
[CLICK] And simply decrement each weight from the individual weight tables.
Thus, by using simple increment and decrement operations, POPET continuously learns from program behavior to accurately predict off-chip loads.

## Slide 107: Latency Configuration
Cache round-trip latency
  L1-D: 5 cycles
  L2: 15 cycles
  LLC: 55 cycles
Hermes request issue latency (incurred after address translation)
Depends on
  Interconnect between POPET and MC
0 cycles
24 cycles
6 cycles
Notes: For our evaluation, we consider
[CLICK] a 5 cycle L1-D
[CLICK] 15 cycle L2
[CLICK] and 55 cycle LLC round-trip latency.
[CLICK] The latency for Hermes to issue a request directly to the main memory controller (after the address translation) depends on …
[CLICK] For this reason we sweep this latency from 0-cycles to 24-cycles in our paper.
[CLICK] But in this presentation, I am going to show you results considering a 6-cycle latency.

## Slide 108: Single-Core Performance Improvement
Chart: Geomean speedup over the No-prefetching system
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | GEOMEAN
Hermes | 1.0966 | 1.1185 | 1.1061 | 1.1108 | 1.1309 | 1.115
Pythia | 1.2123 | 1.2715 | 1.0568 | 1.1992 | 1.2108 | 1.2034
Pythia + Hermes | 1.2628 | 1.3007 | 1.1279 | 1.2388 | 1.2854 | 1.2574
Pythia + Ideal Hermes | 1.292 | 1.3305 | 1.1417 | 1.261 | 1.3239 | 1.2863
11.5%
20.3%
5.4%
Hermes alone provides nearly
50% performance benefits of Pythia with only 1/5th storage overhead
Hermes on top of Pythia
outperforms Pythia alone in every workload category
Hermes provides nearly 90% performance benefit of Ideal Hermes that has an ideal off-chip load predictor
Notes: Let’s first analyze the single-core performance improvement.
[CLICK] This is how Hermes and a state-of-the-art prefetcher Pythia improves performance on top of a no-prefetching system.
[CLICK] The first takeaway is that Hermes alone provides nearly 50%...
[CLICK] Now if we combine Hermes with Pythia, that provides an additional 5.4% performance improvement on top of a strong baseline that has Pythia.
[CLICK] And finally, if we compare Hermes’s performance benefit with the Ideal Hermes that has an ideal off-chip predictor,
We see that Hermes provides nearly 90% performance benefit of the Ideal Hermes

## Slide 109: Increase in Main Memory Requests
Chart: % increase in main memory requests over the No-prefetching system
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
Hermes | 0.056805 | 0.029895 | 0.27038 | 0.072653 | 0.062029 | 0.055441
Pythia | 0.41862 | 0.2408 | 0.48617 | 0.37302 | 0.52323 | 0.38512
Pythia + Hermes | 0.47511 | 0.27921 | 0.65693 | 0.41847 | 0.60518 | 0.44428
5.5%
38.5%
5.9%
11.5%
20.3%
5.4%
For every 1% performance benefit,
increase in main memory requests
Pythia
Hermes on top of Pythia
Hermes alone
2%
1%
0.5%
Hermes is more bandwidth-efficient
than even an efficient prefetcher like Pythia
Notes: This performance improvement comes at a cost of increase in main memory requests.
This graph shows the increase in the main memory request over the no-prefetching system provided by the three configurations.
[CLICK] As we can see, Hermes increases the main memory requests by 5.5% on average on top of the no-prefetching system..
Whereas Pythia increases …
If we combine two together, then it increases the main memory request by an additional 5.9%.
[CLICK] Now, if we compare this increase in the main memory request with the performance improvement each of these configurations are providing,
We see that
[CLICK] For every 1% performance benefit, Pythia …
[CLICK] This basically shows that Hermes is much more bandwidth efficient than a traditional data prefetcher like Pythia.
And for this reason [NEXT]

## Slide 110: Performance with Varying Memory Bandwidth
Chart: Main Memory Bandwidth (in MT/s)
| 200 | 400 | 800 | 1600 | 3200 | 6400 | 12800
Pythia | 0.90608 | 1.0297 | 1.1215 | 1.1842 | 1.2034 | 1.2051 | 1.2044
Hermes | 0.99513 | 1.0581 | 1.0896 | 1.1085 | 1.115 | 1.1174 | 1.1168
Pythia+Hermes | 0.96845 | 1.0682 | 1.1608 | 1.2325 | 1.2574 | 1.2593 | 1.2583
~AMD Threadripper 3990x (Zen 2, 64C/4ch, 2020)
~AMD EPYC Rome 7702P (Zen 2, 64C/8ch, 2019)
~Intel Xeon 6258R
(Cascade Lake, 28C/6ch, 2020)
Pythia
Hermes
Pythia+Hermes
In bandwidth-constrained configurations,
Hermes alone outperforms Pythia
Hermes+Pythia outperforms Pythia
across all bandwidth configurations
Baseline
Notes: If we evaluate Pythia and Hermes over a wide range of memory bandwidth configurations, we see that,
[CLICK] In these extremely-bandwidth constrained configurations, which are in fact roughly modeling per-core main memory bandwidth of commercial processors,
Hermes even outperforms Pythia.
[CLICK] And if we combine both of them, the combination of Hermes and Pythia outperforms Pythia in every bandwidth configurations.

## Slide 111: Performance with Varying Baseline Prefetcher
Chart: Geomean speedup over the No-prefetching system
| Pythia | Bingo | SPP | MLOP | SMS
Prefetcher-only | 1.2034 | 1.1937 | 1.1443 | 1.1347 | 1.0568
Prefetcher + Hermes | 1.2574 | 1.2554 | 1.1948 | 1.2104 | 1.1342
5.4%
6.2%
5.1%
7.6%
7.7%
Hermes consistently improves performance
on top of a wide range of baseline prefetchers
Notes: And these observations are not only true for Pythia.
We evaluate Hermes combined with multiple prior baseline state-of-the-art prefetchers and find that
Hermes consistently improves performance on top of a wide range of baseline prefetchers.

## Slide 112: Overhead of Hermes
4 KB storage overhead
1.5% power overhead*
*On top of an Intel Alder Lake-like performance-core [2] configuration
[2] https://www.anandtech.com/show/16881/a-deep-dive-into-intels-alder-lake-microarchitectures/3
Notes: All of these performance benefit comes at a
[CLICK] modest 4KB storage overhead per core and
[CLICK] 1.5% power overhead on top an Intel Alder Lake-like performance-core configuration

## Slide 113: More in the Paper
Performance sensitivity to:
  Cache hierarchy access latency
  Hermes request issue latency
  Activation threshold
  ROB size (in extended version on arXiv)
  LLC size (in extended version on arXiv)
Accuracy, coverage, and performance analysis against HMP and TTP
Understanding usefulness of each program feature
Effect on stall cycle reduction
Performance analysis on an eight-core system
Notes: We have many more evaluation results:
For example, a wide range of performance sensitivity study by varying…in the paper.

## Slide 114: Initial Set of Program Features

## Slide 115: Selected Set of Program Features
Five features
A binary hint that represents whether or not a cacheblock has been recently touched

## Slide 116: When A Feature Works/Does Not Work?
Trace: 462.libquantum-1343B
PC: 0x401442
Cacheline #42
Cacheline #43
…
…
Without prefetcher
PC + first access
Cacheline offset + first access
With a simple stride prefetcher
Cacheline offset + first access

## Slide 117: What Happens in case of a Misprediction?
Two cases of mispredictions:
Predicted on-chip but actually goes off-chip
  Loss of performance improvement opportunity
Predicted off-chip but actually is on-chip
  Memory controller forwards the data to LLC if and only if a load to the same address have already missed LLC and arrived at the memory controller
No need for misprediction detection and recovery
No need for misprediction detection and recovery

## Slide 118: Performance Headroom of Off-Chip Prediction

## Slide 119: System Parameters

## Slide 120: Evaluated Workloads

## Slide 121: Observation: Not All Off-Chip Loads are Prefetched
Chart: Fraction of off-chip loads in the No-prefetching system
| No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
Blocking | 0.59586 | 0.27156 | 0.50345 | 0.19755 | 0.64046 | 0.42323 | 0.68078 | 0.23748 | 0.71751 | 0.56666 | 0.63334 | 0.35497
Non-blocking | 0.40414 | 0.13884 | 0.49655 | 0.097339 | 0.35954 | 0.12376 | 0.31922 | 0.10632 | 0.28249 | 0.2031 | 0.36666 | 0.14188
MPKI | 16.72 | 8.4511 | 19.6554 | 4.7661 | 9.5423 | 5.7169 | 18.2326 | 8.423 | 20.7412 | 10.4891 | 18.0321 | 7.9886
50%
Nearly 50% of the loads are still not prefetched
1

## Slide 122: Observation: Not All Off-Chip Loads are Prefetched
Chart: Fraction of off-chip loads in the No-prefetching system
| No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
Blocking | 0.59586 | 0.27156 | 0.50345 | 0.19755 | 0.64046 | 0.42323 | 0.68078 | 0.23748 | 0.71751 | 0.56666 | 0.63334 | 0.35497
Non-blocking | 0.40414 | 0.13884 | 0.49655 | 0.097339 | 0.35954 | 0.12376 | 0.31922 | 0.10632 | 0.28249 | 0.2031 | 0.36666 | 0.14188
MPKI | 16.72 | 8.4511 | 19.6554 | 4.7661 | 9.5423 | 5.7169 | 18.2326 | 8.423 | 20.7412 | 10.4891 | 18.0321 | 7.9886
70% of these off-chip loads blocks ROB
2

## Slide 123: Observation: With Large Cache Comes Longer Latency
On-chip cache access latency significantly contributes to the latency of an off-chip load
Chart: # stall cycles due to an off-chip load blocking instruction retirement from ROB
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
On-chip cache access latency | 58.4907 | 63.496 | 55.0896 | 61.496 | 56.0957 | 58.9336
Remaining | 76.5749 | 74.4995 | 96.2024 | 100.5303 | 94.7627 | 88.1545
58
On-chip cache hierarchy access latency

## Slide 124: Observation: With Large Cache Comes Longer Latency
On-chip cache access latency significantly contributes to the latency of an off-chip load
Chart: # stall cycles due to an off-chip load blocking instruction retirement from ROB
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
On-chip cache access latency | 58.4907 | 63.496 | 55.0896 | 61.496 | 56.0957 | 58.9336
Remaining | 76.5749 | 74.4995 | 96.2024 | 100.5303 | 94.7627 | 88.1545
58
On-chip cache hierarchy access latency
40% of stall cycles caused by an off-chip load can be eliminated
by removing on-chip cache access latency from its critical path

## Slide 125: What Fraction of Load Requests Goes Off-Chip?

## Slide 126: Off-Chip Prediction Quality: Defining Metrics
Predicted off-chip
Actual off-chip
Predicted and actual off-chip
Accuracy
Coverage

## Slide 127: Off-Chip Prediction Quality: Analysis
Accuracy
Coverage
Chart: Accuracy %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.4412 | 0.40588 | 0.49015 | 0.32147 | 0.61767 | 0.47032
TTP | 0.11337 | 0.11045 | 0.16348 | 0.11497 | 0.27204 | 0.16612
POPET | 0.82929 | 0.77941 | 0.72326 | 0.79347 | 0.73138 | 0.77141
Chart: Coverage %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.2149 | 0.17874 | 0.2214 | 0.09024 | 0.34055 | 0.22308
TTP | 0.95587 | 0.95967 | 0.94187 | 0.9398 | 0.94131 | 0.94785
POPET | 0.77488 | 0.67572 | 0.83355 | 0.69819 | 0.76205 | 0.74276
47%
22%
16%
95%
77%
74%

## Slide 128: Off-Chip Prediction Quality: Analysis
Accuracy
Coverage
Chart: Accuracy %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.4412 | 0.40588 | 0.49015 | 0.32147 | 0.61767 | 0.47032
TTP | 0.11337 | 0.11045 | 0.16348 | 0.11497 | 0.27204 | 0.16612
POPET | 0.82929 | 0.77941 | 0.72326 | 0.79347 | 0.73138 | 0.77141
Chart: Coverage %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.2149 | 0.17874 | 0.2214 | 0.09024 | 0.34055 | 0.22308
TTP | 0.95587 | 0.95967 | 0.94187 | 0.9398 | 0.94131 | 0.94785
POPET | 0.77488 | 0.67572 | 0.83355 | 0.69819 | 0.76205 | 0.74276
47%
22%
16%
95%
77%
74%
POPET provides off-chip predictions with high-accuracy and high-coverage

## Slide 129: Effect of Different Features
Combination of features provides both higher accuracy and higher coverage than any individual feature

## Slide 130: Are All Features Required? (1)
No single feature individually provides
highest prediction accuracy across all workloads

## Slide 131: Are All Features Required? (2)
No single feature individually provides
highest prediction coverage also across all workloads

## Slide 132: Single-Core Performance
Hermes in combination with Pythia
outperforms Pythia alone in every workload category

## Slide 133: Single-Core Performance Line Graph

## Slide 134: Single-Core Performance Against Prior Predictors
POPET provides higher performance benefit
than prior predictors
Hermes with POPET achieves nearly 90% performance improvement of the Ideal Hermes

## Slide 135: Effect on Stall Cycles
Hermes reduces off-chip load induced stall cycles
on average by 16.2% (up-to 51.8%)

## Slide 136: Eight-Core Performance
Hermes in combination with Pythia
outperforms Pythia alone by 5.1% on average

## Slide 137: Effect of Hermes Request Issue Latency
3.6%
5.7%
Hermes in combination with Pythia outperforms Pythia alone even with a 24-cycle Hermes request issue latency

## Slide 138: Effect of Cache Hierarchy Access Latency
3.6%
6.2%
Hermes can provide even higher performance benefit in
future processors with bigger and slower on-chip caches

## Slide 139: Effect of Activation Threshold
With increase in activation threshold
Accuracy increases
Coverage decreases

## Slide 140: Power Overhead

## Slide 141: Effect of ROB Size
6.7%
5.3%

## Slide 142: Effect of LLC Size
1.3%
2.5%

## Slide 143: Accuracy and Coverage with Different Prefetchers
POPET’s accuracy and coverage increases significantly
in absence of a data prefetcher

## Slide 144: Increase in Main Memory Requests

## Slide 145: Increase in Main Memory Requests

## Slide 146: Hermes Limit Study

## Slide 147: Athena Discussions

## Slide 148: Athena Discussions
Motivational data
Features considered
Q-Value table organization
Final configuration
Overhead analysis
Simulation parameters
Evaluated workloads
Evaluated mechanisms
Perf in CD1
Perf in CD2
Perf in CD3
Perf in CD4
Prefetcher sensitivity
OCP sensitivity
Bandwidth sensitivity
Four-core perf
Eight-core perf
Impact of uncorrelated reward
Understanding Athena

## Slide 149: Motivational Data

## Slide 150: Motivational Data

## Slide 151: Features Considered

## Slide 152: Q-Value Table Organization

## Slide 153: Final Configuration

## Slide 154: Overhead Analysis

## Slide 155: Simulation Parameters

## Slide 156: Evaluated Workloads

## Slide 157: Evaluated Cache Designs

## Slide 158: Evaluated Mechanisms

## Slide 159: Performance Gain in CD1

## Slide 160: Performance Gain in CD2

## Slide 161: Performance Gain in CD3

## Slide 162: Performance Gain in CD4

## Slide 163: Sensitivity to Prefetcher Type

## Slide 164: Sensitivity to OCP Type

## Slide 165: Sensitivity to Main Memory Bandwidth

## Slide 166: Performance Improvement in Four-Core

## Slide 167: Performance Improvement in Eight-Core

## Slide 168: Impact of Uncorrelated Reward

## Slide 169: Understanding Athena

## Slide 170: Constable Discussions

## Slide 171: Constable Discussions
Motivation & Design
Why do global-stable loads exist?
Effect of increasing registers
Characterization of global-stable loads
Resource dependence by global-stable loads
Performance headroom
Constable overview
Architecting elimination table
Effect of wrong-path update
Example of Constable’s operation
Ensuring coherence
Storage overhead
Area/energy overhead
Methodology & Evaluation
Simulation parameters
Evaluated workloads
Workload-wise performance
Load-category-wise performance
Comparison with prior works
Elimination coverage
Coverage of global-stable loads
Reduction in power
Scaling width
Scaling depth
Violating memory ordering

## Slide 172: Why Do Global-Stable Loads Exist?
Random* Random::s_rng = 0;
Random* Random::get_Rng(void)
{
if (s_rng == 0)
s_rng = new Random();
return s_rng;
}
Example code from 541.leela_r
Global scope variable
Function to access the variable
Notes: To answer that, here is an example code from a SPEC CPU workload.
[CLICK] The code declares a global-scope variable and
[CLICK] its access function.

## Slide 173: Why Do Global-Stable Loads Exist?
Random* Random::s_rng = 0;
Random* Random::get_Rng(void)
{
if (s_rng == 0)
s_rng = new Random();
return s_rng;
}
624: mov rax, [rip+0x1f4ac5]
62b: test rax,rax
62e: je 0x638
630: ret
631: nop
638: sub rsp,0x8
63c: mov edi,0xc
641: call 0x460
Example code from 541.leela_r
Disassembly (compiled by GCC* with –O3)
*GNU GCC 13.2
Notes: Here is the disassembly of the code compiled by latest GCC with full optimization.

## Slide 174: Why Do Global-Stable Loads Exist?
Random* Random::s_rng = 0;
Random* Random::get_Rng(void)
{
if (s_rng == 0)
s_rng = new Random();
return s_rng;
}
624: mov rax, [rip+0x1f4ac5]
62b: test rax,rax
62e: je 0x638
630: ret
631: nop
638: sub rsp,0x8
63c: mov edi,0xc
641: call 0x460
Example code from 541.leela_r
Gets initialized only once
and never changes
Global-stable load
Disassembly (compiled by GCC* with –O3)
*GNU GCC 13.2
Notes: If we focus on the highlighted “if” instruction, it gets converted to a load instruction to read the global variable, followed by a branch.
[CLICK] Now, as the variable gets initialized only once and never gets changed,
[CLICK] the corresponding load instruction naturally becomes a global-stable load
that always fetches the same data from the same address.

## Slide 175: Why Do Global-Stable Loads Exist?

## Slide 176: Why Do Global-Stable Loads Exist?
Global-stable loads exist for many reasons:
Accessing global variables
Accessing local variables of an inline function
Limited architectural registers
...

## Slide 177: Effects of Increasing Architectural Registers
Fraction of global-stable loads
are nearly same without or with APX
Compiled with Clang 18.1.3 with and without -mapxf

## Slide 178: Effects of Increasing Architectural Registers
Fraction of global-stable loads (i.e., Constable’s opportunities)
are much higher than reduction in loads by APX
Compiled with Clang 18.1.3 with and without -mapxf

## Slide 179: Effects of Increasing Architectural Registers
The profile of global-stable loads stays largely unchanged
after doubling registers using APX

## Slide 180: Characterization of Global-Stable Loads (I)

## Slide 181: Characterization of Global-Stable Loads (II)

## Slide 182: Characterization of Global-Stable Loads (III)

## Slide 183: Resource Dependence by Global-Stable Loads
Global-stable loads cause significant resource dependence

## Slide 184: Performance Headroom Analysis

## Slide 185: Constable Overview

## Slide 186: Architecting SLD

## Slide 187: Effect of Wrong-Path Update

## Slide 188: An Example of Constable’s Operation

## Slide 189: Ensuring Coherence
Constable relies on snoop requests to observe modifications to a memory address by other cores

## Slide 190: Ensuring Coherence
Constable relies on snoop requests to observe modifications to a memory address by other cores
Evicting a cacheline from core-private cache resets the core-valid bit in directory
  What if a clean eviction?
    Unnecessary elimination opportunity loss
Constable pins the CV-bit of an eliminated load’s cacheline
  Even if the cacheline gets evicted from core-private cache, snoop request gets delivered

## Slide 191: Constable’s Storage Overhead

## Slide 192: Area and Power Overhead of Constable’s Structures

## Slide 193: Simulated System Parameters

## Slide 194: Evaluated Workloads

## Slide 195: Workload-Wise Performance

## Slide 196: Load Category-Wise Performance

## Slide 197: Performance Comparison with Prior Works

## Slide 198: Elimination Coverage

## Slide 199: Coverage of Global-Stable Loads

## Slide 200: Reduction in Dynamic Power

## Slide 201: Performance Sensitivity to Load Execution Width Scaling

## Slide 202: Performance Sensitivity to Pipeline Depth Scaling

## Slide 203: Eliminated Loads that Violates Memory Ordering
Only 0.09% of all eliminated loads
violate memory ordering

## Slide 204: Eliminated Loads that Violates Memory Ordering
Eliminated loads that violate memory ordering
increase number of allocated instructions only by 0.3%